Programming a line-follow robot

Embedded Software - Robot Lab

Group Number: 25
Student 1:
Thijs Boumans, 4214854
Student 2:
Stephan Neevel, 4232623

# Introduction
The report is about programming a line-follow robot. The setup of the robot is the following: a smartphone is placed on the robot. This smartphone uses its camera to record the line. These images are sent to the laptop via wifi and are then processed to detect a line. The laptop sends directions to the robot via bluetooth and the robot will drive and follow the line based on these commands. There is also an ultrasonic sensor facing to the front of the robot. When it detects something, the robot should stop in time not to bump into something.
The report will cover the requirements of the programming, testing whether the H-bridge is active low or high, the used timer settings on the Arduino. It will also cover the message structure of the so called Twist message and how the motors react to this. Next comes the line detection algorithm and how the Twist messages are constructed based on this.

# Requirements
To develop a clear basis for the programming of the robot, requirements have been drawn. These are divided in functional and non-functional requirements.

Functional requirements
-The robot can drive around based on geometry_msgs/Twist messages published on the topic cmd_vel.

-The robot will stop when an object of at least 4 cm width and 3 cm height is placed within 20 cm in front of it, so it doesn't collide with it. Due to form of the tracks on the robot, we estimated that the robot can drive over objects that are a maximum of 3 cm high. Also, from our experience using the HC -SR04 ultrasonic sensor, we noted it can reliably 'see' objects of 4 cm width within 1 meter distance.

-The robot should be able to drive at different speeds based on the geometry_msgs/Twist messages published on the topic cmd_vel. It should remain able to meets its other requirements.

-The robot is able to follow the line in 4 different test tracks. One of the tracks contains lines crossing each other, and the robot should be able to cope with this. The line can be as little as 0.4 cm wide, Furthermore, the sum of the difference between the background and the line of all three RGB channels could be as little as 90. A bit of testing with different RGB values and experience with other line following robots, we came to this number.

-The timers in the Arduino sketch are set via the AVR timing registers.

-The speed of the robot is adjusted based on the distance to the robot in front when several
robots drive on the same test track. The minimal distance to the robot in front should always be 20 cm. We estimate this is a safe distance to avoid collision.

-The robot must stop when no new commands have been given to the Arduino from the laptop for a time of 2 seconds. This is to avoid the robot from going rogue.

-The ROS line-follow node should be independent of the implementation of the robot; it just uses the geometry_msgs/Twist messages and publishes it on the topic cmd_vel.

Non-functional
-The line follow setup will consist of an android smartphone, a robot with Arduino, and a laptop working together.
-The software should be independent of laptop choice and android smartphone choice.
-The roundtrip delay from the smartphone, to the laptop to the Arduino can be as high as 100 ms. We estimated that with a high disturbance, and a short distance of the wifi and bluetooth, this is a reasonable number.

# Testing the H-bridge

# Used timer settings on the Arduino

# Twist-message to motor-interface mapping

# The line detection algorithm

When the picture of the line arrives on the computer, an algorithm processes it to discover the line and send a Twist message back to the robot. The algorithm first starts by scaling, rotating and warping the image. The picture arrives on its side, so to make viewing possible it is rotated in the right direction. To improve the speed of the algorithm, the picture is scaled down by 90 percent, to a picture of 128*72 pixels. The smartphone is placed at an angle in the robot, so lines that are parallel on the track will not be parallel on the image. To adjust for this and get the lines parallel again , the picture is warped.
INSERT EXAMPLE HERE

# The algorithm for generating the Twist messages